Title
WCET'2008
Computing Time as a Program Variable:
a
infeasible paths
Niklas Holsti
Tidorum Ltd
www.tidorum.fi
way
around

---
Example: Saturating a value
Make sure that x is between 1 and 10:
if x < 1 then x := 1; end if;
if x > 10 then x := 10; end if;
if x < 1
x := 1
Infeasible combination of
- (new) value of x and
- value of condition x > 10
end if;
x := 10
if x > 10
The path that executes both assignments x := 1 and x := 10 is infeasible
This is the longest path
 overestimated WCET
end if;

---
Reasoning
Infeasible paths arise from dependencies (correlations) between variable values/assignments
and values of branch conditions
Some analysis of such dependencies is necessary
Earlier work: “path-oriented” analysis
  - find (in-) feasible combinations of CFG blocks/edges
  - use “flow facts” to constrain eg. IPET
Suggestion: “value-oriented” analysis
  - find (in-) feasible combinations of variable values
  - make execution time a variable, T
  - thus, find (in-) feasible execution times = values of T
infeasible path
infeasible value of T

---
From values to feasible WCET
Path-oriented:
dependencies
between values
of vars/conds
feasible
paths
WCET for
feasible paths
specific analysis of
(in)feasible paths
bounds calculation
eg. by IPET
Value-oriented:
dependencies
between values
of vars/conds
including T
feasible
values of T
dependency-sensitive value analysis

---
Adding the T variable (in a real tool)
Add T to the internal representation (CFG) of the machine-code program
Add T := 0 at the start of the program/subprogram
Add T := T + t(b) in each basic block b
  - t(b) comes from processor-behaviour analysis
    - using all structural paths in the CFG
    - may include infeasible paths
Ditto for control-flow edges that take some time
Use interval arithmetic if t(b) is not a single value
  - eg. context-dependent pipeline or cache effects

---
Adding T to the “saturation” example
Add T as a variable in the (pseudo-) source code
Add else-parts to model the condition-evaluation time.
T := 0;
if x < 1 then x := 1; T := T + 3;
        else T := T + 1; end if;
if x > 10 then x := 10; T := T + 3;
        else T := T + 1; end if;
ET of program = final value of T
  - Infeasible path ET is 3 + 3 = 6 cycles.
  - WCET is 1 + 3 = 4 cycles.
  - BCET is 1 + 1 = 2 cycles.

---
A dependency-sensitive value-analysis
This is just one method/domain; others are possible
  - similar to the analysis in the Bound-T WCET tool,
  - which Bound-T currently uses mainly for loop bounds
  - implemented with the Omega Calculator (Pugh et al.)
Models:
  - value of one variable : integer  Z
  - combined values of n variables : n-tuple  Z n
  - all combined values of n variables : n-tuple set  Z n
  - instruction : transfer relation  Z n  Z n = Z 2n
Set : { [v1,v2,...,vn] | constraints }
Relation : { [v1,v2,...,vn]  [v'1,v'2,...,v'n] | constraints }
Constraints in Presburger Arithmetic form: Presburger sets

---
Presburger-set analysis of the example
pre-value set
 {[x,T]}
 T := 0;
instruction
post-value set
 {[x,0]}
 {[x,0] | x ≥ 1}
if x < 1 ...
 {[x,0] | x < 1}
x < 1
x ≥ 1
x := 1;
T := T + 3;
T := T + 1;
 {[x, 1] | x ≥ 1}
 {[1, 3]}
 {[x,1] | x ≥ 1}  {[1,3]}
 {[x,1] | 1 ≤ x ≤ 10}  {[1,3]}
if x > 10 ...
 {[x,1] | x > 10}
T := T + 1;
x := 10;
T := T + 3;
3;
x ≤ 10
x > 10
 {[10, 4]}
 {[x,2] | 1 ≤ x ≤ 10}  {[1,4]}
 {[x, 2 ] | 1 ≤ x ≤ 10}  {[1, 4 ]}  {[10, 4 ]}

---
What about loops?
Three different things:
  - finding loop bounds (bounds on # of iterations)
  - finding the effect of loops on variable values
  - handling infeasible paths involving loops.
Presburger-set analysis can be used for all three things
Focus: how T -variable works in infeasible looping paths
initial values
loop
head
repetition values
post-loop (exit) values

---
The repetition relation of a loop
The repetition relation of a loop shows how variable values change in one repetition of the loop
  - from the transfer relations of the instructions in the loop
  - exit from loop is treated separately (as normal flow)
Example: Reverse order of vec[n .. n + 9]:
i := n; j := n + 9;
while i < j loop
   z := vec[i]; vec[i] := vec[j]; vec[j] := z;
   i := i + 1;
   j := j – 1;
end loop;
Ignore the vec[] values (pointer analysis...)
The repetition relation R for i, j, n, z is:
  - R = { [ i, j, n, z ]  [ i + 1, j – 1, n, z' ] | i < j }

---
Invariant, induction, and fuzzy variables
Use the repetition relation R to classify each variable v as:
  - invariant:	R does not change v
  - induction:	R sets v := v + dv, where dv is constant  Z \{0}
  - fuzzy:	R changes v in other (unknown) ways
Computation: see paper
  - intersect R with { [v, dv]  [v + dv] }
  - project to dv
  - take convex hull  interval of possible dv
Example above:
  - i and j are induction variables; di = 1, dj = -1
  - n is invariant; in other words dn = 0
  - z is fuzzy.

---
Induction model of loop
Add iteration counter c = 0, 1, ...
Induction model: Value of v at start of iteration c is
  - if invariant:	v = v0 = initial value of v
  - if induction:	v = v0 + c  dv
  - if fuzzy:	v is unconstrained (unknown)
Loop bound N: see paper
  - propagate the induction model to the back edge:
  - { [i, j, n, z] | i – 1 < j+1 and i = n+1+c and j = n+8+c }
  - project to c
  - take convex hull  bounds on c that allow repetition
  - example: c  4.
Post-loop values: Propagate induction model to exit
  - effect on induction variable: v := v + N  dv , N constant
    - plus possible effect of the loop-exit path

---
T is an induction variable
Effect of loop is T := T + N  dT
  - dT is the execution time of one loop repetition
  - N is a constant (range)
dT from dependency-sensitive analysis of loop body
  - excludes infeasible paths contained in the loop body
    - when infeasibility is iteration-independent
dT is a Presburger variable
  - can depend on other variables
  - shows dependency between paths inside and outside loop
  - final T excludes infeasible combinations of such paths
    - when infeasibility is iteration-independent
Hard to handle iteration-specific infeasibility
Fails for infeasible “path – loop-bound” combinations

---
Example iteration-independent case
T := 0;
if x < 1 then T := T + 100;
        else T := T + 10;
end if;
for i in 1 .. 7 loop
   if x > 3 then T := T + 200;
        else T := T + 20;
   end if;
end loop;
contradictory
conditions
apply in the same way on each loop iteration
x is invariant
No path can take the slow case of both branches
  - infeasible longest path = 100 + 7  200 = 1500 cycles
  - longest feasible path = 10 + 7  200 = 1410 cycles
T-analysis works; final T = 1410.

---
Summary
Add execution-time variable T
  - T becomes “entangled” with other variables/conditions
Use dependency-sensitive value-analysis
  - final value of T is “entangled” with feasible paths
Good:
  - no specific analysis and representation of infeasible paths
  - handles many kinds of infeasible paths
Bad:
  - history-sensitive t(b) may be over-estimated
  - Presburger-set analysis is costly; hard to scale up
Possible future work:
  - implementation and evaluation
  - other, cheaper dependency-sensitive value-analyses
    - but non-convexity (disjunction) is probably desirable